## Slide 1: Next Generation Electrical Energy Storage Basic Research Needs (BRN) Workshop
Report to the Basic Energy Sciences Advisory Committee
Esther Takeuchi
July 13, 2017
Workshop held March 27-29, 2017
Workshop Chair: George Crabtree, Univ. of Illinois-Chicago/ANL
Co-Chairs: Gary Rubloff, University of Maryland
Esther Takeuchi, Stony Brook University/BNL

## Slide 2: Fundamental breakthroughs in chemical & materials sciences are essential to transform the energy landscape
LLNL flowcharts available from https://flowcharts.llnl.gov
Quad = 1015 BTU; 2007 consumption ≈ 2015 consumption (~3.3 terawatts)

## Slide 3
Basic Research Needs (BRN) Workshops
BRN to Assure a Secure Energy Future BESAC (2002)
  BRN for Hydrogen Economy (2003)
  BRN for Solar Energy Utilization (2005)
  BRN for Superconductivity (2006)
  BRN for Solid State Lighting (2006)
  BRN for Advanced Nuclear Energy Systems (2006)
  BRN for Geosciences (2007)
  BRN for Clean and Efficient Combustion (2007)
  BRN for Electrical Energy Storage (2007)
  BRN for Catalysis for Energy Applications (2007)
  BRN for Materials under Extreme Environments (2007)
  BRN for Carbon Capture (2010)
  New Science for Sustainable Energy Future (2008)
  Computational Materials Science and Chemistry (2010)
  Science for Energy Technology (2010)
  Controlling Subsurface Fractures and Fluid Flow (2015)
  BRN for Environmental Management (2016)
  BRN for Quantum Materials (2016)
  BRN on Synthesis Science for Energy Relevant Technology (2017)
18 reports; 15 years; >2,000 participants from academia, industry, and DOE labs
2002
https://science.energy.gov/bes/community-resources/reports/

## Slide 4: Batteries and Energy Storage Cross-Cutting Challenge that Impacts Energy
Grid reliability and distributed power require innovative energy storage devices
  Enhancing grid resiliency in case of disruptive events and demand peaks
  Storage of large amounts of power
  Delivery of significant power rapidly
Transportation requires next generation batteries
  Providing higher energy and power densities, longer drive distance
  Longer lifetimes, faster recharge times
  Enabling greater communication and connection with information and guidance systems
Battery safety has emerged as cross-cutting research topic
Scientific tools for battery research have seen significant advancement

## Slide 5
Next-Generation Electrical Energy Storage BRN
Given the transformative opportunity in 2017 and beyond to utilize electrical energy storage in diverse applications far beyond personal electronics, the workshop was designed to:
    Provide an assessment of the current status of electrical energy storage.
    Identify the highest priority basic science gaps and opportunities in our fundamental understanding.
    Define the new insights and innovations needed from basic research in materials science and chemistry to enable future scientific and technological advances for next-generation electrical energy storage.
  Workshop held March 27-29, 2017 with 175 scientists representing theory, simulation, characterization, electrochemistry and synthesis in attendance.
Computer model of ion movement in a membrane
Atomic resolution of a solid electrolyte
Neutron imaging of batteries in operation
Combined imaging techniques track chemical changes

## Slide 6
NG-EES BRN: Plenary Speakers
Electrical Energy Storage: Where have we come from and the scientific challenges still facing us?
– M. Stan Whittingham, Binghamton University
High-energy batteries: a systems perspective
– Karen Thomas-Alyea, Samsung Research America
Challenges for Solid State Batteries
– Linda Nazar, University of Waterloo
Nanoscience for Energy Storage:
Success and Future Opportunity
– Yi Cui, Stanford University
Materials science for electrochemical storage: Achievements and new directions
– Jean-Marie Tarascon, Collège de France

## Slide 7
Next-Generation Electrical Energy Storage BRN
Six (6) panels discussed scientific challenges spanning existing and next generation electrochemical energy storage structures, the experimental and theoretical tools and techniques to explore them, and promising emerging architectures and approaches to achieve them.
Pathways to simultaneous high energy and power
  Structure, interphases, and charge transfer at electrochemical interfaces
  In pursuit of long lifetime and reliability: Time-dependent phenomena at electrodes and electrolytes
  Discovery, synthesis and design strategies for materials, structures, and architectures
  Solid-state and semi-solid electrochemical energy storage
  Cross-cutting themes

## Slide 8
NG-EES BRN: Panel Leadership
Panel 1: Pathways to Simultaneous High Energy and Power - Paul Braun, University of Illinois at Urbana-Champaign, and Jun Liu, Pacific Northwest National Laboratory
Panel 2: Structure, Interphases, and Charge Transfer at Electrochemical Interfaces - Lynden Archer, Cornell University, and David Prendergast, Lawrence Berkeley National Laboratory
Panel 3: In pursuit of long lifetime and reliability: Time-dependent Phenomena at Electrodes and Electrolytes - Shirley Meng, University of California-San Diego, and Jay Whitacre, Carnegie Mellon University
Panel 4: Discovery, Synthesis, and Design Strategies for Materials, Structures, and Architectures - Perla Balbuena, Texas A&M University, and Amy Prieto, Colorado State University
Panel 5: Solid-State and Semi-Solid Electrochemical Energy Storage - Nancy Dudney, Oak Ridge National Laboratory, and Jeff Sakamoto, University of Michigan
Panel 6: Crosscutting Themes: Yue Qi, Michigan State University, Eric Stach, Brookhaven National Laboratory, and Mike Toney, SLAC

## Slide 9: Workshop Approach
Each panel developed a list of critical research areas.
On day 2, the research areas were evaluated and grouped into topics according to five Priority Research Directions.
The panel leads and members joined the relevant Priority Research Direction (PRD) group.
The PRD teams met to formulate the research approaches and thrust areas.
Day 3, report out and writing of PRDs and Panel reports.

## Slide 10
PRD1: Tune Functionality of Materials and Chemistries to Enable Holistic Design for Energy Storage
+
+
+
Anode
Cathode
Separator
+
+
e
_
current collector
(SEI)
Solid-electrolyte interphase
electrolyte
Holistic design of architectures and components
Maximum performance with minimum complexity
Consider full cell action and interaction at the outset
Multifunctional materials
Many functions from one material
May combine ion mobility and electronic conductivity
Overcome paradigm of one material one function

## Slide 11
Thrust 2: Multifunctional Solid State Electrolytes
Thrust 3: New Battery Chemistries
Anode
Electrolyte
Cathode
Concentric tube 3D battery
• Short transport lengths
• High surface area
• Large volume
Thrust 1: Simultaneous High Energy and High Power
MRS Bull., 2011, 36, 523
Amorphous Li
Li Al5O8
Li in metal
Li
Al
O
C
High ionic conductivity
Low electronic conductivity
Inhibit dendrite growth
Nat. Mater., 2017,16, 572
Multivalent electrode materials
Challenge in adopting new multivalent materials is understanding of charge storage and transport mechanisms
Focus on abundant and low cost elements
PRD1: Tune Functionality of Materials and Chemistries to Enable Holistic Design for Energy Storage
Challenges:
• Low interfacial impedance
• Predictive interfacial simulation
Chem. Mater., 2015, 27, 10, 3609

## Slide 12
PRD 2—Link Complex Electronic, Electrochemical, and Physical Phenomena across Time and Space
Cathode
SEI
Electrolyte
+
+
+
Bulk Solvation
Ionic Conduction
Intercalation
Desolvation
+
Mobility and local strain
The opportunity is to characterize multiple coupled electro-chemical-mechanical phenomena over
diverse time and length scales
A comprehensive suite of multi-modal tools is needed to capture coupled electrochemical phenomena
• in situ observation
Multiscale modeling
PNAS, 2016, 113, 10779
X-Ray ptychography
Acc. Chem. Res., 2013, 46, 5, 1216
M. Toney, unpublished.
Multiscale phenomena
Dendrite Growth
Courtesy LLNL

## Slide 13
PRD 2—Link Complex Electronic, Electrochemical, and Physical Phenomena across Time and Space
Thrust 2: integrate computational and characterization tools
Thrust 1: Create state-of-the-art modeling techniques and characterization tools
Models of coupled
electro-chemical-mechanical battery phenomena
complexity
length scale
DFT
DFTB
ReaxFF
-MD
PFF-MD
Phase Field
ESIC
e– transfer
Li+ transfer
SEI formation & evolution
JACS, 2012, 134, 15476
TEM
TOF-SIMS
Organic layer
Li2CO3
Pore diffusion
w / anion
Interstitial knock-off
wo / anion
organic
Li2CO3
Li2CO3
LiF
Depth (nm)
6Li/7Li ratio
Two layer mesoscale Li+ diffusion model
Informed by TEM and TOF-SIMS
Space charge mediated by LiF/Li2CO3 interfacial defects
Tune Li+ conductivity by LiF/Li2CO3 volume ratio and grain size
LiF
Li2CO3
Computationally designed artificial SEI
ACS Appl. Mater. Interfaces, 2016, 8, 5687
Acc. Chem. Res., 2016, 49, 2363
JACS, 2011, 133, 14741
J. Phys. Chem. C, 2014, 118, 18362
J. Electrochem. Soc., 2004,151,11, A1977

## Slide 14: PRD 3: Control and exploit the complex interphase region formed at dynamic interfaces
Mechanical, chemical, electrical processes at interface evolve with emergent, different properties.
Informed design of interfaces can produce beneficial interphases.
Targets
Widen stability window of liquid electrolytes
Understand, control electric potentials at solid state battery interfaces
Design, Synthesis and Characterization of Functional Interfaces
Create relevant model systems for learning and theory validation
New characterization methodologies
Beneficial interphases from synthesized coatings, possibly with active or adaptive functionalities
Courtesy of ANL
J. Electrochem. Comm. 2012, 24, 43
E. J. Fuller and A. A. Talin, unpublished

## Slide 15: PRD 3: Control and exploit the complex interphase region formed at dynamic interfaces
Thrust 1. Unravelling interfacial complexity through in-situ and operando characterization and theory
Well-controlled model systems
Intrusive interrogation of realistic and working systems
Operando X-ray and neutron methods
Thrust 2: Designing SEI for function
Understand ion transport in interphases
Interphase design and controlled synthesis
Self-healing to mitigate degradation
Science, 2016, 353, 566
ACS Cent. Sci., 2017, 3, 5, 399

## Slide 16: PRD 4: Revolutionize energy storage performance through innovative assemblies of matter
New architectures to reduce passive content and capacity fade
Materials synthesis, processing, assembly from nano to meso
Informed by hierarchical modeling/simulation and in-situ/ operando experimental results
Courtesy Wei Wang and Vijayakumar Murugesan, PNNL

## Slide 17: PRD 4: Revolutionize energy storage performance through innovative assemblies of matter
Thrust 1. Design and Synthesize New Mesoscale Architectures
Smart, multiscale architectural design
Reverse design: synthesis to achieve multiple properties
Architectures informed by experimental databases and machine learning
Thrust 2: Develop New Concepts for Large-Scale Energy Storage and Conversion
Rethinking flow batteries
Electrocatalytic chemical energy storage
Manipulating solvation
Membranes and interfaces tailored to new redox chemistries
Solid State Ionics, 2004, 175, 243
Energy Environ. Sci., 2014, 7, 3307
Nat. Commun. 2015, 6, 7259.

## Slide 18: PRD 5: Promote Self-healing and Eliminate Detrimental Chemistries to Extend Lifetime and Improve Safety
Full understanding of the degradation pathways occurring during battery life
  when and where degradation events occur
  how rapidly they advance
  new approaches to slow or stop them and to design around them
J. Power Sources, 2017, 341, 373
  systematic and precise study
  new tools and sensors
  more sophisticated simulation
Safer and more robust devices without sacrificing energy density or performance

## Slide 19: PRD 5: Promote Self-healing and Eliminate Detrimental Chemistries to Extend Lifetime and Improve Safety
Thrust 1 – Multimodal in-situ experiments to quantify degradation and failure.
Identify key degradation and failure mechanisms.
Determine roles of inhomogeneity and nonlinearities.
Discover mitigation strategies.
Thrust 2 – Multi-physics, multi-scale, predictive continuum models for degradation and failure
Use modeling and characterization in combination with representative and model systems.
Develop and implement predictive multiscale models and continuum models.
J. Electrochem. Soc., 2017, 164, A304
Nat. Comm., 2015, 6, 6924

## Slide 20
Next-Generation Electrical Energy Storage BRN
Current Status
Brochure providing a high level summary of the workshop has been released.
Workshop final report is in preparation.
Content of report:
  Priority research directions
  Panel reports
  Factual document