## Slide 1: Computing for a new era
John Paul Strachan, Miao Hu, Cat Graves, Suhas Kumar, Naveen Muralimanohar, Dejan Milojicic, R. Stanley Williams
BESAC Meeting July 13, 2017

## Slide 2
The end of Moore’s law could be the best thing that has happened in computing since the beginning of Moore’s law.
What’s Next?

## Slide 3: Future exponential increases in computer performance and efficiency will require multiple advances:
Memory-centric computing – no von Neumann bottleneck
Gen-Z – high performance open fabric to democratize computing
(http://genzconsortium.org/ - ~40 companies so far)
Dot-product engine: memristor-based vector-matrix multiplication accelerator for neural nets and signal processing
Chaos as a computing resource for constrained optimization problem solving (Hopfield network)
Systems and
Architectures
Devices

## Slide 4
GPU
DSP
x86
ASIC
TPU
Neuro
Quantum
POWER
SPARC
RISC V
ARM
FPGA
Memory
From processor-centric computing…
the traditional von Neumann architecture
Memory
Memory
Memory
Memory
Memory
Memory
Memory
Memory
Memory
Memory
Memory
Memory
SoC
SoC
SoC
SoC
SoC
SoC
SoC
SoC
SoC
SoC
SoC
SoC
…to Memory-Driven Computing
with Gen-Z open (nonproprietary) fabric, computing is plug and play

## Slide 5: Memory-Driven Computing (MDC) is a reality: The Machine
Combining memory and storage in a stable environment to increase processing speed and improve energy efficiency
Using photonics where necessary to eliminate distance and create otherwise impossible topologies
Optimizing processing from general to specific tasks
Radically simplifying programming and enabling new applications that we can’t even begin to build today
Fast, persistent memory
Fast memory fabric
Task-specific processing
New and Adapted
software
Memristor technology, ongoing transfer from lab to commercial product
Developing new accelerators from novel device behavior
Gen-Z fabric: ultra-high bandwidth open bus to democratize computing
Up to 8000x speed-up for Monte Carlo simulations

## Slide 6
Parallel multiply & add through Kirchoff’s and Ohm’s laws
      1961, K. Steinbuch “Die Lernmatrix“– suggests using “ferromagnetic toroids”
Memristors as highly scalable, tunable analog resistors
    High ON/OFF ratio (~105), supporting multiple levels
Well suited for streaming workloads like neural nets
Many ways to scale up
  Memristor levels, array size, wire pitch, 3D layer, DAC/ADC speed & width etc.
Performance (execution time) improvements >1000x and
energy efficiency >100x over GPUs for particular applications
Commercial products in development
IjO= ∑i Gij . ViI
Input Voltage vector
Output current
Dot Product Engine: memristor arrays accelerate vector-matrix multiplication

## Slide 7
Can Li, in preparation
Time-domain inputs (applied to rows)
Freq-domain (DCT) outputs (read from columns)
Real-time experimental
data from DPE
Software cosine transform
Experimental Demo - Signal processing on DPE system
(UMass collaboration) – instantaneous cosine transform
  C. Li, et. al, manuscipt under review

## Slide 8: NbO2 memristor: computing with nonlinear dynamics and chaos
nanoscale oscillator
=
Frequency analysis
Oscillations -
Chaos
Dynamical Behavior:
Lyapunov exponent
in situ and in operando
scanning transmission
x-ray microscopy (STXM)
at ALS critical for analysis
of memristor operation

## Slide 9: Chaos enabled Hopfield network for optimization problems
S Kumar, et al. Nature, in press
Traveling Salesman problem:
Synapses
Memristor DPE
Neurons
Chaotic NbO2 nanodevices
Find shortest route visiting all cities
Γ=0 (no chaos)
Example solutions w/ and w/o chaos

## Slide 10: Acknowledgments
HPE Labs
Miao Hu
Suhas Kumar
Catherine Graves
Emmanuelle Merced
Dejan Milojicic
Ali Shafiee
Naveen Muralimanohar
Stan Williams
Jianhua Yang
Qiangfei Xia
Can Li
Yunning Li
Izzat El Hajj (UIUC)
Pedro Bruel (IME)
David Kilcoyne
David Vine
Johanna Weker
Hendrik Ohldag
Funding assistance

## Slide 11: Synchrotron at LBNL
The Advanced Light Source (ALS) at Lawrence Berkeley National Laboratory
To study the very small, we had to use the very large